## Slide 1: SWARM ROBOTICS AND ITS APPLICATIONS
Presented by
Chinmay Mahabal
Rutvij Pathak
Pratik Shende
Internal guide
Mrs.A.A.Mate

## Slide 2: Introduction
Swarm robotics is a new approach to the coordination of multirobot systems which consist of large numbers of mostly simple physical robots. It is supposed that a desired collective behavior emerges from the interactions between the robots and interactions of robots with the environment. This approach emerged on the field of artificial swarm intelligence, as well as the biological studies of insects, ants and other fields in nature, where swarm behavior occurs.

## Slide 3: Types of Swarms
HETEROGENEOUS SWARM
HOMOGENEOUS SWARM

## Slide 4: Biology to Robotics
Swarm of birds
Swarm of robots

## Slide 5: Other Swarm Robot Projects : -
Colias Project
Jasmine Swarm Robot Project
Kilobot

## Slide 6: References :-
7.1 REFERENCES:
7.1.1 JOURNAL PAPERS:
[1] Y. Xinan, L. Alei, and G. Haibing, "An algorithm for self-organized aggregation of swarm robotics using timer," in Swarm Intelligence (SIS), 2011 IEEE Symposium on, 2011, pp. 1-7. [2] L. Bayindir and E. Sahin, "A review of studies in swarm robotics,"Turkish Journal of Electrical Engineering, vol. 15, pp. 115-147, 2007.
[3] Kilobot: A Low Cost Scalable Robot System for Collective Behaviors
Michael Rubenstein, Christian Ahler, Radhika Nagpal
IEEE Intl. Conf on Robotics and Automation (ICRA), 2012.
7.1.2 BOOK REFERENCES:
[1] Swarm Intelligence and Algorithms by Yuhui Shi.
[2]Muhammad Ali Mazidi, “AVR Microcontroller and Embedded System”, 14 august 2011, 1st
edition.
7.1.3 WEB
1. www.techdocs.altium.com/display/FPGA/NEC+IR+TX+PROTOCOL
2. http://www.swarm-bots.org
3. http://www.eecs.harvard.edu/ssr/projects/progSA/kilobot.html

## Slide 7: Our Goal : -
To develop a hardware platform which is simple ,cost effective and easy to manufacture .
To develop a basic autonomous agents using various algorithms and protocols ,which will lead to the development of basic A.I .
Proposed Design of the Agent

## Slide 8: Block Diagram of an Agent
MAPPING
MICROCONTROLLER
(Atmega328p)
MOTOR DRIVER
(L293D)
IR LED
IR RECIEVER (TSSOP)
MOTORS
(3 V , 200 RPM)

## Slide 9: Environment
Proposed Environment for testing of the swarm

## Slide 10: Environment
The environment will be constructed out polystyrene .
Various obstacles will be placed in the environment .
Figure Illustrates the proposed environment
The obstacles are represented by blue .

## Slide 11: Applications
The swarm robots are used in disaster rescue and emergency situations where multiple agents (robots) are deployed in time critical situations ,where numbers are an advantage.
Swarm robots are also used in artificial intelligence research as an hardware platform to implement algorithms .

## Slide 12: Applications be presented :-
Follow the leader – This indicates the ability of the group to follow without being explicitly programmed .
Cluster Formation - This is precursor to self-assembly it demonstrated the ability to organize into group .

## Slide 13: 1 .Follow the leader
In this experiment the users will define a leader among the group of bots .
All the other bots will “follow the leader” by either imitating the leader robot or forming a line behind it and follow him from point A to Point B .
They will not only follow the leader’s direction but the imitate its every action.
The leader bot is designated by red .
Robots assembled behind a leader

## Slide 14: 2.Cluster Formation
In this experiment the users will define a specific shape to be formed .
After receiving the command ,the robots will form a specific shape around a robot which will be considered a “seed robot ”.
The seed robot in the diagram is indicated by red .
Cluster formations are precursors for self-assembly which is an emerging field in robotics.
Example of a cluster formed a seed robot

## Slide 15: Construction of an Agent - Level 1
This level contains the base on which the entire agent will be built .
This level contains a base , 4 standoff screws , 2 motors and wheel assembly .
This is also the level on which battery will be placed , for optimum balance .

## Slide 16: Construction of an Agent-Level 2
This level contains the main microprocessor which will be controlling the agent’s behavior .
This level has 4 pairs of transmitters and receiving IR .
These IR transmitters and receivers are used for mapping the surrounding environment .
Alternatively these can also be used for communication .
Phototransistor and IR emitter pair (VSMB10940) will be used for odometry .

## Slide 17: Construction of an Agent-Level 3
Proposed design of the agent
This is the topmost layer of the agent.
This level contains 4 transmitters and receiver pair .
These pairs will be used for communication.

## Slide 18: Actual Construction of an Agent

## Slide 19: NEC Protocol
The NEC IR transmission protocol uses pulse distance encoding of the message bits. Each pulse burst (mark – RC transmitter ON) is 562.5µs in length, at a carrier frequency of 38kHz (26.3µs). Logical bits are transmitted as follows:
Logical '0' – a 562.5µs pulse burst followed by a 562.5µs space, with a total transmit time of 1.125ms
Logical '1' – a 562.5µs pulse burst followed by a 1.6875ms space, with a total transmit time of 2.25ms

## Slide 20: Work Done in Semester 1 :-
Tasks Completed : -
Arduino Agent assembly
Ultrasound Sensor Testing
IR communication Setup

## Slide 21: PCB (zero pcb)
Initial Zero PCB designs

## Slide 22: Version 1
Actual Photo of the PCB
Eagle layout of the proposed PCB

## Slide 23: Version 2
Eagle layout of the proposed PCB
Actual Photo of the PCB

## Slide 24: Version 3

## Slide 25
Actual photo of the final Agent

## Slide 26: Various Iteration of the base of the agents

## Slide 27: Transistor Testing Setup
Input output Waveform Comparison
Transistor triggering delay measured
Transistor testing assembly

## Slide 28: THANK YOU !